## Slide 1: Introduction – MPR121 chip from NXP
12 channels for capacitive sensor electrodes
LED drive available on 8 out of 12 channels (only 1-2 LEDs / channel)
Autoconfig: fits to wide range of electrode sizes automatically
Baseline Tracking (BT) - adjusts Baseline Value (BV) to changes in environment
Electrode signal
Signal Filter
Baseline
Filter
BV# – EV#
>?
TH
Baseline filter parameters
# Electrode Value
(EV#)
BV#
Set as parameter if BT off
Threshhold parameter (TH)
Yes
# touched!
No
# not touched.

## Slide 2: Application 1 – proximity with layout A
row1
row2
array
ring
ELE1: active shielding + proximity
ELE0: touch + proximity
MPR121
Capacitive sensing
LED power supply
MCU
Arduino
I2C
row1, 2 and ring:
PWM duty cycle („on-time”) proportional to surface area touched  prop. to radiance
5-9V DC
ELE2, 3, …#: active shielding
array:
ON/OFF if proximity sensed
PWM
ON/OFF

## Slide 3: Application 1 – proximity with layout A
PX check
>?
PX shielding
Yes
No
Touch Intensity
TI# = BV# – EV#
touch weights (t#)
Proximity (PX) check = TI0*w0 + TI1*w1
PX shielding = TI2*w2 + TI3*w3 +…
PX value =
PX check - PX shielding
T check
>?
T shielding
proximity weights (w#)
Touch (T) check = I0*t0
Touch (T) shielding = TH + TI1*w1 + TI2*w2 + …
Yes
PX value = 0
T value =
T check – T shielding
T value = 0
No
PX value
>?
PX TH
PX threshhold
No
Yes
LED array ON
LED array OFF
Duty cycle = scaled(T value)
LED row1, 2 and ring ON
LED row1, 2 and ring OFF
active shielding

## Slide 4: Applications 2, 3 - with layout „Round”
5-9V DC
ELE1…7: functions
ELE0: ON/OFF
MPR121
Capacitive sensing
LED power supply
MCU
Arduino
I2C
LEDs in 1 ring on 2 separate tracks: inwards and outwards facing LEDs.
ELE8, 9, …#: active shielding
8 transparent capacitive touch areas
PWM
ON/OFF
0

## Slide 5: Application 2 – slider
Turning on: 3x short blinks
Turning off: one long blink
No
Yes
0 touched!
Wait
Turning on!
No
Yes
2 | 4 | 6
touched!
Outwards duty cycle = scaled (T value 2 + 4 + 6)
1 | 3 | 5 | 7
touched!
Inwards duty cycle =
scaled (T value 1 + 3 + 5 + 7)
active shielding
Turning off!
Outwards LEDs ON
Inwards LEDs ON
Is it ON?
Is it ON?
others touched?
Yes
Yes
Inwards LEDs OFF
Outwards LEDs OFF
active shielding
No
No
Is it ON?

## Slide 6: Application 3 – sine wave
Turning on: 3x short blinks
Turning off: one long blink
No
Yes
Wait
Turning on!
0 touched!
No
Yes
Turning off!
others touched?
Is it ON?
1 touched!
No
Yes
others touched?
Is it ON?
No
Yes
Wait
Any LEDs ON?
Increase
PWM duty cycle (radiance)
Yes
Inwards + Outwards sine wave ON
No
2 touched! | 3 touched! | 4 touched! | 5 touched! | 6 touched! | 7 touched!
Decrease radiance | ON/OFF sine wave Outwards | ON/OFF sine wave Inwards | Double freq. of sine wave | Halve freq. of sine wave | „Sampling” if sine ON: 3 blinks, @ π/3, π/2, (2π)/3
Touch button 2, 3…7 similarly.
Function table:

## Slide 7: Application 4 – turnwheel/dialing
Turning on: 3x short blinks
Turning off: one long blink
Inwards, Outwards facing LEDs
receive the same PWM duty cycle.
„T value # decreasing?  No” flow mirrors „Yes” flow exhibited: „next” and „prev” touch values are also tested to detect movement direction – ClockWise (CW) or CounterClockWise (CCW).
others touched?
No
Yes
Wait
Turning on!
0 touched!
No
Yes
Is it ON?
# touched!
No
Yes
Is it ON?
Wait
active shielding
CW movement, ++ PWM duty cycle!
CCW movement,
-- PWM duty cycle (radiance)
T value #
decreasing?
T value (#+1) increasing?
(„next”)
Yes
Turning off!
Yes
T value (#-1) increasing?
(„prev”)
No
Yes
No
No

## Slide 8: Application 4 – turnwheel/dialing
Inwards, Outwards facing LEDs
receive the same PWM duty cycle.
„T value # decreasing?  Yes” flow mirrors „No” flow exhibited: „next” and „prev” touch values are also tested to detect movement direction – ClockWise (CW) or CounterClockWise (CCW).
Turning on: 3x short blinks
Turning off: one long blink
CW movement example:
Wait
CCW movement, -- PWM duty cycle!
CCW movement,
++ PWM duty cycle (radiance)
T value (#+1) decreasing?
(„next”)
T value (#-1) decreasing?
(„prev”)
No
T value #
decreasing?
Yes
Yes
No
No
Yes
active shielding
T value
„time”
ELE(#+1)
ELE(#)
ELE(#-1)
++ PWM
++ PWM